## Slide 1: Environment Impact Assessment (EIA) Notification 2006
Information Sources:
1.) Environment Impact Notification 2006; Gazette of India, 14th September, 2006
2.) Green Tapism; Environment Support Group; 2007
3.) Image of tree from http://www.cherrytreebooks.net/Images/CTBooksTreeLogo.gif

## Slide 2: Underlying basis, spirit and preamble
Protect environment and control pollution
Environment Protection Act 1986 (May 1986)
Environment Protection Rules 1986 (Nov 1986)
  Section 5 Environment Protection Rules 1986: Prohibitions and restrictions on the location of industries; carrying on of processes and operations in different areas
EIA 1994
  Environment Protection Act 1986
  Discharge internationally agreed obligations under Rio Declaration
EIA 2006 is supersession of EIA 1994, except in respect of things done or omitted to be done before such supersession
complimentary

## Slide 3: EIA 2006 - Preamble
Copies of the said notification were made available to the public on 15th September, 2005
Objections and suggestions received in response to the above mentioned draft notification have been duly considered by the Central Government
Central Government hereby directs that on and from the date of its publication (14th September, 2006)
    the required construction of new projects or activities or the expansion or modernization of existing projects or activities listed in the Schedule to this notification entailing capacity addition with change in process and or technology shall be undertaken in any part of India only after the prior environmental clearance from the Central Government or as the case may be, by the State Level Environment Impact Assessment Authority, duly constituted by the Central Government under sub-section (3) of section 3 of the said Act, in accordance with the procedure specified hereinafter in this notification.

## Slide 4: Categorization of projects and activities
All projects and activities are broadly categorized in to two categories - Category A and Category B
  spatial extent of impacts
  impacts on natural and man made resources
  impacts on human health
Go to schedule of notification and show project list

## Slide 5: Requirements of prior Environmental Clearance (EC)
Which projects require EC?
  Projects listed in the schedule to notification (as Category A and B projects)
  All new projects or activities listed in the Schedule to this notification
  Expansion and modernization of existing projects or activities listed in the Schedule to this notification
  Any change in product - mix in an existing manufacturing unit included in Schedule

## Slide 6: Requirements of prior Environmental Clearance (EC)
EC by whom?
  Category A projects: Central Government in the Ministry of Environment and Forests
    Base decisions on the recommendation by Expert Appraisal Committee (EAC)
  Category B projects: At state level the State Environment Impact Assessment Authority (SEIAA)
    The SEIAA shall base its decision on the recommendations of a State or Union territory level Expert Appraisal Committee (SEAC) as to be constituted for in this notification
    In the absence of a duly constituted SEIAA or SEAC, a Category ‘B’ project shall be treated as a Category ‘A’ project

## Slide 7: State Level Environment Impact Assessment Authority (SEIAA)
SEIAA shall be constituted by the Central Government
  comprising of three Members
  Chairman and a member–secretary to be nominated by the State Government or the Union territory Administration
  Rules for membership of SEIAA
  All decisions of the SEIAA shall be unanimous and taken in a meeting

## Slide 8: Expert Committees for Screening, Scoping and Appraisal (EAC and SEAC)
Expert Committees
  Expert Appraisal Committees (EACs) at the Central Government
  State Expert Appraisal Committees (SEAC) at the State or the Union territory
Responsible for screening, scoping and appraising projects
Procedure for selection and maintenance of EAC and SEAC is given in notification

## Slide 9: Application for Prior Environmental Clearance
An application seeking prior environmental clearance in all cases shall be made
  In the prescribed Form 1 and Supplementary Form 1A
  After the identification of prospective site(s)
  After identification of activities
  Submit pre-feasibility report for all and conceptual plan for construction activities

## Slide 10: Stages in EC process
Stage 1: Screening (Only for Category ‘B’ projects and activities)
Stage 2: Scoping
Stage 3: Public Consultation
Stage 4: Appraisal
Sequential order
all of which may not apply to particular cases as set forth in this notification

## Slide 11: Stage 1: Screening
Only for Category B projects and activities to determine if they need EIA
Category A projects compulsorily need EIA
Scrutiny of an application seeking EC by SEAC for determining whether or not the project or activity requires further environmental studies
  Form 1
  Form 1A
Classify projects as B1 (require EIA) and B2 (don’t require EIA)
For categorization of projects into B1 or B2, the MoEF shall issue appropriate guidelines from time to time

## Slide 12: Stage 2: Scoping
Who does the scoping?
  Expert Appraisal Committee (EAC) in the case of Category ‘A’ projects or activities
  State level Expert Appraisal Committee (SEAC) in the case of Category ‘B1’ projects
Determine comprehensive Terms Of Reference (TOR) addressing all relevant environmental concerns for preparation of an Environment Impact Assessment (EIA) Report based on
  on the basis of the information furnished by applicant in the prescribed application Form1/Form 1A including
  proposed by the applicant
  a site visit by a sub- group of EAC or SEAC only if considered necessary

## Slide 13: Stage 2: Scoping
In the case of Category A Hydroelectric projects TOR shall be conveyed along with the clearance for pre-construction activities
If TOR not finalized and conveyed to the applicant within sixty days of the receipt of Form 1, TOR suggested by the applicant shall be deemed as the final TOR approved for the EIA studies
Approved TOR shall be displayed on the website of the MoEF or the concerned SEIAA
Applications for EC may be rejected at this stage itself
  the decision together with reasons for the same shall be communicated to the applicant
Prepare EIA draft report

## Slide 14: Stages in EC process
Stage 1: Screening (Only for Category ‘B’ projects and activities)
Stage 2: Scoping
Stage 3: Public Consultation
Stage 4: Appraisal
Sequential order
all of which may not apply to particular cases as set forth in this notification

## Slide 15: Stage 3: Public consultation
Process by which the concerns of local affected persons and others who have plausible stake in the environmental impacts of the project or activity are ascertained
All Category ‘A’ and Category B1 projects or activities shall undertake Public Consultation
  A big list of exceptions

## Slide 16: Stage 3: Public consultation
Public Consultation shall ordinarily have two components
  public hearing at the site or in its close proximity- district wise, to be carried out in the manner prescribed in Appendix IV, for ascertaining concerns of local affected persons
  obtain responses in writing from other concerned persons having a plausible stake in the environmental aspects of the project

## Slide 17: Component 1: Public hearing
Public hearing shall be conducted by the State Pollution Control Board (SPCB)
  forward proceedings to the regulatory authority concerned within 45 days
  If not appoint another independent organization to do the same within another 45 days
If the public agency nominated reports that it is not possible to conduct the public hearing in a manner which will enable the views of the concerned local persons to be freely expressed
  It shall report the facts in detail to the concerned regulatory authority
  After due consideration of the report shall rule that the public consultation in the case need not include the public hearing

## Slide 18: Component 2: Responses from other concerned persons
Invite responses from such concerned persons by placing on their website the Summary EIA report
Use other appropriate media for ensuring wide publicity about the project
Within seven days of the receipt of a written request for arranging the public hearing
Confidential information including non-disclosable or legally privileged information involving Intellectual Property Right shall not be placed on the website
Make available on written request from any concerned person the Draft EIA report for inspection at a notified place during normal office hours till the date of the public hearing
All the responses received as part of this public consultation process shall be forwarded to the applicant through the quickest available means

## Slide 19: After public consultation…
Applicant shall address all environmental concerns expressed during this process
Make appropriate changes in the draft EIA
Final EIA report shall be submitted by the applicant to the concerned regulatory authority for appraisal

## Slide 20: Stages in EC process
Stage 1: Screening (Only for Category ‘B’ projects and activities)
Stage 2: Scoping
Stage 3: Public Consultation
Stage 4: Appraisal
Sequential order
all of which may not apply to particular cases as set forth in this notification

## Slide 21: Stage 4: Appraisal
Detailed scrutiny by the EAC or SEAC of
  documents like the Final EIA report
  outcome of the public consultations including public hearing proceedings
  submitted by the applicant to the regulatory authority concerned for grant of environmental clearance
Appraisal of all projects or activities which are not required to undergo public consultation, or submit an Environment Impact Assessment report (Category B2) shall be carried out on the basis
    prescribed application Form 1
    Form 1A
    any other relevant information

## Slide 22: Stage 4: Appraisal
EAC or SEAC shall
  shall recommend to the regulatory authority concerned
    either for grant of prior environmental clearance on stipulated terms and conditions
    or rejection of the application for prior environmental clearance, together with reasons for the same.
Prescribed procedure for appraisal is given in Appendix V

## Slide 23: Grant or Rejection of EC
The regulatory authority shall consider the recommendations of the EAC or SEAC concerned and convey its decision to the applicant
The regulatory authority shall normally accept the recommendations of the Expert Committees
In cases where it disagrees with the recommendations of the Expert Committee (Central or State), the regulatory authority shall request reconsideration by the Central or State Expert Appraisal Committee
After reconsideration, irrespective of views of Expert Committee, decision of the regulatory authority concerned shall be final

## Slide 24: Grant or Rejection of EC
If decision not granted within stipulated time, the applicant may proceed as if the environment clearance sought for has been granted or denied by the regulatory authority in terms of the final recommendations of the Expert Committee concerned
Deliberate concealment and/or submission of false or misleading information or data which is material to screening or scoping or appraisal or decision on the application shall make the application liable for rejection
Rejection of an application or cancellation of a prior environmental clearance already granted shall be decided by the regulatory authority, after giving a personal hearing to the applicant, and following the principles of natural justice

## Slide 25: Validity of Environmental Clearance
Ten years in the case of River Valley projects
Thirty years for mining projects
Five years in the case of all other projects and activities
Area Development projects and Townships, the validity period shall be limited only to such activities as may be the responsibility of the applicant as a developer

## Slide 26: Post Environmental Clearance Monitoring
Mandatory for the project management to submit half-yearly compliance reports in respect of the stipulated prior environmental clearance terms

## Slide 27: Summary of EIA process and Rough Timelines
Submission of application (Form 1, prelim reports)
Stage 1: Screening; Decide project A, B1 or B2
Stage 2: Scoping; Come up with Terms of Reference (TOR)
Prepare preliminary EIA report
Stage 3: Public consultation (2 components)
Stage 4: Appraisal
Final Decision
60 days
45 days
60 days
15 days
30 days
Investor
Expert Committee
Investor
State Pollution Control Board
Expert Committee
Regulatory Authority
Who does it?
Update EIA report (Investor)

## Slide 28: Loopholes and deficiencies
Stage 1 - Screening
  Based on info (form 1, 1A) supplied by investor
  Pre-feasibility report and conceptual plan - no guidelines or requirements, thereby no need to address environmental issues
Stage 2 - Scoping
  No public participation in scoping process - local knowledge about what environmental concerns should be investigated is not given consideration
  Strict timeline – not a continuous process
  Biased in securing favorable Terms of Reference (TOR) for investors
  Access to TOR limited

## Slide 29: Loopholes and deficiencies
Stage 3 – Public consultation
  Unclear wording and definitions
    Can be avoided if regulatory agency feels it difficult to conduct it owing to local situation
    local affected persons having plausible stake in impact of project
    Public consultation shall ordinarily have two components
    Other concerned persons having plausible stake shall submit responses only in writing
    Hearing shall be conducted at the site or in its close proximity
  No quorum required for holding public consultation
  Huge list of exemptions for certain types of projects that cause deep environmental impact without justification
    Weak wording that widens the scope of these exemptions
  Tight timeline: 45 days from the time requested by the investor

## Slide 30: Loopholes and deficiencies
  Limiting access to information
    Only summary EIA report made available, not the full EIA with all TOR from the scoping process
    Confidential information need not be disclosed in summary EIA
  Publicity
    Use of internet as the main means
    No definition on how publicity should be carried out
  Erosion of constitution of panel conducting public hearing
    EIA 2006 mentions only District Magistrate and a representative of SPCB
    EIA 1994 had District Collector, representatives of state dealing with the project, reps from panchayats, senior citizens from the area, reps of SPCB

## Slide 31: Loopholes and deficiencies
Appraisal
  No public participation
  Arguments between regulatory authority and expert committee made known only to investor and not to public
  Iron hand given to regulatory authority to make final decision – Expert committee opinion can be disregarded
  Deemed Clearance: Incase decision is not given within the prescribed timelines, applicant may proceed as though clearance has been granted or denied

## Slide 32: Summary of EIA process and Rough Timelines
Submission of application (Form 1, prelim reports)
Stage 1: Screening; Decide project A, B1 or B2
Stage 2: Scoping; Come up with Terms of Reference (TOR)
Prepare preliminary EIA report
Stage 3: Public consultation
Stage 4: Appraisal
Final Decision
60 days
45 days
60 days
15 days
30 days
Investor
Expert Committee
Investor
State Pollution Control Board
Expert Committee
Regulatory Authority
Who does it?
Update EIA report (Investor)